## Slide 1: The Benefits of Automated Boiler Blowdown
Presented by:

## Slide 2
“Chemical treatment programs that are not
accompanied by effective blowdown
monitoring are one of the leading causes of
excessive boiler operating efficiencies
and/or failure.”
-- Kewanee Boiler Company
        Source: www.kewaneeboiler.com
How Important is Routine Surface Blowdown?

## Slide 3
Under the worst cases, manual blowdown leads to high and low conductivity spikes
Above the target maximum forms scale
Below the target maximum wastes water
Inadequacies of Manual Boiler Blowdown

## Slide 4
Manual Blowdown Could Lead to Excess Water Usage
At best, manual blowdown results in far lower than ideal conductivity levels
This results in excess water usage

## Slide 5
Excessive Blowdown Has Many Costs
Water costs -- Excessive blowdown means
more makeup and higher sewage bills
Energy costs -- Heated water is sent down the
drain during blowdown
Chemical costs -- Chemical usage is, in most
cases, directly tied water usage

## Slide 6
Scale Formation Leads to Energy Inefficiency
Infrequent blowdown leads to scale forming conductivity levels
1/1000” layer of scale reduces heat transfer efficiency by up to 10%
Extreme scale build-up leads to costly repairs/replacements

## Slide 7
Benefits of Automatic Boiler Blowdown
Conductivity levels are monitored continuously
Conductivity is kept near the target maximum at all times

## Slide 8
Automated Boiler Blowdown Saves Money
Minimum of 20% increase in conductivity levels versus manual control. This would result in a 20% direct savings in fuel.
Less blowdown and makeup required
Less makeup means less chemical usage
Less testing and manual care required
Prevents costly scale formation -- big savings !!!
Average payback time of less than one year

## Slide 9
Types of Boiler Controllers: Continuous Sampling
Used only when steam blowdown requirements exceed 5000 pounds per hour
Allows a continuous sample of water to flow across the probe (to drain) and continuously monitors and adjusts the conductivity levels
Only used on the largest of boilers due to the continual flow of sample water to drain

## Slide 10
Types of Boiler Controllers: Timed Sampling
Used when steam blowdown is less than 5000 pounds per hour
Controller intermittently takes a sample of boiler water and blows down until conductivity falls to desired levels
Most commercial and light industrial applications use timed sampling

## Slide 11
Typical Timed-Sampling Blowdown Installation

## Slide 12: Any Questions?